## Slide 1: Digital Engineering 1
Lecture 3

## Slide 2: Truth Table

## Slide 3: Boolean Algebra
Named after George Boole
Axioms
  0 · 0 = 0
  0 + 0 = 0
  0’ = 1
Duality
  1 · 1 =1
  1 + 1 = 1
  1’ = 0
0 + 1 = 1 + 0 = 1
0·1 = 1·0 = 0

## Slide 4: Single Variable Theorems
x | · | 0 | = 0
x | + | 1 | = 1
x | · | 1 | = x
x | + | 0 | = x
x | · | x | = x
x | + | x | = x
x | + | !x | = 1
x | · | !x | = 0
x | · | x | x · … x = x
!!x = x

## Slide 5: Two Variable Theorems
x | · | y | = | y | · | x
x | + | y | = | y | + | x
Both are commutative

## Slide 6: Three Variable Theorems
Associative Laws
Distributive Law
x · (y + z) = (x
· y) + (x · z)
x + (y · z) = (x + y) · (x + z)
x | · | (y | z) | = | (x | · | y) | · | z
x | + | (y | + z) | = | (x | + | y) | + | z

## Slide 7: DeMorgan’s Theorem
 X1  X2  ...  Xn
X1  X2  ...  Xn   X1  X2  ...  Xn
X1  X2  ...  Xn 
X  Y  X  Y
X Y  X Y
Note that

## Slide 8: Proof Techniques
(Example 1)
Prove x + (y·z) = (x + y) · (x + z)
RHS = x · (x+z) + y · (x+z)
= x·x + x·z + y·x + y·z
= x·(1+z+y) + y·z
= x·(1)+ y.z
= x + y.z
Fairly Straightforward

## Slide 9: Proof Techniques
(Example 1)
Prove x + (y·z) = (x + y) · (x + z)
RHS = x · (x+z) + y · (x+z)
= x·x + x·z + y·x + y·z
= x·(1+z+y) + y·z
= x·(1)+ y.z
= x + y.z
Fairly Straightforward

## Slide 10: Proof Techniques
(Example 2)
Prove x + x · y = x
= | x | (1 | + | y)
= | x | ·1 |  | 
= | x |  |  | 
Introduce a constant
x + x · y = x · 1 + x · y

## Slide 11: Proof Techniques
(Example 3)
Prove x.y + y.z + x’.z = x.y + x’.z
LHS = x.y + y.z.1 + x’.z
= x.y + y.z.(x+x’) + x’.z
= x.y + y.z.x + y.z.x’ + x’.z
= x.y (1 + z) + (y + 1) .x’.z
= x.y + x’.z
Introduce a constant and introduce a function

## Slide 12: Boolean Techniques
(Example 4)
Simplify x.y + x.y.z + y.z
LHS | = | x.y | + | x.y.z | + | y.z
 | = | x.y | + | x.y.z | + x.y.z | + y.z
= x.y (1 + z) + y.z (x + 1)
= x.y + y.z
= y.(x+z)
Introduced a copy of a term
A simpler derivation is there. Think about it!

## Slide 13
Prove the Two Variable Theorems Below
Absorption
x | + | (x | · | y) | = | x
x | · | (x | + | y) | = | x
Combining
  x · y + x · y’ = x
  (x + y)· (x + y’) = x
DeMorgan’s Laws
(x + y)’ = x’· y’
(x · y)’ = x’+ y’

## Slide 14: Boolean Functions
x2

## Slide 15: Design Problem 1
Design a circuit for staircase light control using a two-way switch
  If both switches are OFF or ON, light is off
  If one of them is ON and another is OFF, the light is ON
System
Truth table

## Slide 16: Design Problem 1
Logic Network
XOR gate

## Slide 17: Design Problem 2
Design a circuit which realizes the following truth table
f = ?

## Slide 18: Design Problem 2 (contd.)
f = x1’.x2’ + x1’.x2 +x1.x2
x1
x2

## Slide 19: Let’s simplify it
f
x1 x2