## Slide 1: Digital Engineering 1
Lecture 5

## Slide 2: Digital Logic Gates

## Slide 3: AND/OR CIRCUITS
Simplest type of combinational logic design consists of inverters, AND gates, and OR gates. This is known as an AND/OR circuit.
An AND/OR circuit can be designed to implement any function by performing the following steps:
  Put the expression in SOP form
  Form complemented literals with inverters
  Form product terms with AND gates.
  Sum the product terms with an OR gate

## Slide 4: Example

## Slide 5: Universality
All Boolean functions can be implemented using the set {AND, OR, NOT}.
Universal gates
  Gates which can implement any Boolean function without the need to use any other type of gate
  NAND and NOR are universal gates
To show universality of a gate: Show that AND, OR and NOT can be implemented using that gate

## Slide 6
AND, OR and NOT can be implemented using NAND only

## Slide 7: Assignment
Show that NOR gate is a universal gat
Show that XOR gate is a universal gat

## Slide 8: Boolean Expression  Truth Table
To convert Boolean expression to truth table: Expand the expression into the minterms (i.e., canonical SOP form) and enter 1’s in truth table rows (or, expand into canonical POS and enter 0’s for each maxterm)

## Slide 9: Truth Table  Boolean Expression
To convert a truth table to a boolean expression:
Write a canonical SOP expression that consists of all minterms (or write a canonical POS using maxterms) and then simplify the algebraic expression.

## Slide 10: Truth Table  Boolean Expression
When the expressions get more complicated, simplification gets harder
You may miss out combinations
More inputs, more the effort
Systematic way to reduce effort
  Karnaugh Maps

## Slide 11: Rearranging Truth Tables

## Slide 12: In General

## Slide 13: Karnaugh Maps
Truth tables are a convenient form to represent equations but they don’t aid in the simplification of logic equations.
Karnaugh maps (K-maps) are similar to TT’s and they lead to graphical methods for Boolean expression simplification.
A K-map is a multi-dimensional tabulation of function values.
Each minterm is assigned an entry (a cell) in the table. The cell contains the value of the function for the corresponding minterm.

## Slide 15: 3-variable K-map: f(a,b,c)
OR

## Slide 16: 4-variable K-map: f(a,b,c,d)

## Slide 17: K-map Example 1

## Slide 21: K-map Example 2

## Slide 23: K-Map Properties
Minterms mapped to any two adjacent cells differ in exactly one bit position

## Slide 24
The sum of two minterms in adjacent cells can be simplified to a single product (AND) term with one less variable.
If we combine adjacent minterms in the first column we get,
That is, variable a is eliminated.

## Slide 25
variable c is eliminated.

## Slide 26: K-Map Based Minimization
The purpose of using K-maps is to aid in the simplification of logic expressions.
Use of 1’s in K-maps gives minterm SOP form directly. Use of 0’s in K-maps gives maxterm POS form directly.
Minterms (maxterms) that can be combined differ in exactly one bit position.
Minimization using K-maps is done by grouping “adjacent” minterms (maxterms).

## Slide 27: Conditions for grouping
Minterm (maxterm) groups are restricted to have size that is a power of 2, e.g., 1, 2, 4, 8, …
All K-map cells in a group must have a 1 as their K-map entry for grouping minterms (or 0 as their K-map entry for maxterm groups).
All minterms (maxterms) must be adjacent; they must differ in exactly i bits where, 2i is the size of the group.

## Slide 28
To minimize a function, find the set of groups which include all the required minterms; the function is the sum of these groups (or if maxterms are used then the function is the product of the groups).
The larger the groups, the better.

## Slide 29: Example: Grouping Minterms
Simplified Expression:
f(w,x,y,z) =  x z  wyz

## Slide 30: Example: Grouping Maxterms

## Slide 31
 | 00 | 01 | 11 | 10
0 | 1 | 0 | 1 | 1
1 | 1 | 0 | 0 | 1
x
yz
 | 00 | 01 | 11 | 10
0 | 1 | 0 | 1 | 1
1 | 1 | 0 | 0 | 1
x
yz
Sum of Products
Product of Sums

## Slide 32: Logic Minimization: Example 2
 | 00 | 01 | 11 | 10
00 | 0 | 1 | 0 | 0
01 | 0 | 1 | 1 | 0
11 | 1 | 1 | 1 | 1
10 | 1 | 1 | 0 | 0
wx
yz