## Slide 1: Digital Engineering 1
Lecture 7

## Slide 2: Combinational Circuits
Output is only dependent on the current input.
Need not know past history of values
Basic gates like AND, OR, NOT, NAND, NOR, XOR, XNOR are all combinational

## Slide 3: Combinational Logic Design
Problem Analysis
Representation
Implementation
Notes: Understand the Problem:
  input/output behavior
  identify the inputs, outputs, and control signals
  draw a top level block diagram if necessary
Formulate in a Standard Representation:
  truth tables or Boolean equations
Choose an Implementation:
  discrete logic gates
  programmable logic devices: PAL, PLA, ROM, FPGA
Apply the Design Procedure:
  follow the representation → minimization → implementation algorithm mechanically
  simulate your circuit before implementing it on actual devices
  implement it on actual devices and verify your implementation.

## Slide 4: Example: Process Line Control
Design a controller to select right length metal rods out of rods of varying length (±10%) traveling one at a time on a conveyor belt. Rods that are within spec. (±5%) remain on the belt. Rods that are too short or too long are discarded by mechanical arm(s).

## Slide 5
a | b | c | Reject
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | X
1 | 1 | 0 | 0
1 | 1 | 1 | 1
in spec
too long
too short

## Slide 6: Building Blocks for Combinational Circuits
Decoders
Encoders
Multiplexers
Demultiplexers

## Slide 7: Decoders
Binary-to-Decimal decoder: n inputs, 2n outputs (n x 2ndecoder). Some decoders have enable inputs.
Each output represents a minterm of an n-variable function.
The output that corresponds to the minterm that appears on the inputs is asserted (active low or high depending upon the device), all other outputs are inactive.

## Slide 8: Decoder

## Slide 9: Build a 4x16 decoder using 2x4 decoders (decoder tree)

## Slide 10: Implementing Logic using Decoders
Decoders can be used to implement logic functions as follows:

## Slide 11: BCD-7 Segment Decoder

## Slide 12: Encoders
Encoder is opposite of decoder. Its output code has fewer bits than the input code.
Binary Encoder: Input: 1-out-of-2n code (decimal input). Output: n-bit binary code.

## Slide 13: Multiplexers
Multiplexing means transmitting a large number of information units over a smaller number of channels or lines.
A digital multiplexer (MUX) selects binary information from one of many input lines and directs it to a single output line.
  Data selector (2n:1 MUX).
  Inputs: 2n data inputs, n select lines.
  Output: 1 data output line.

## Slide 14: 2:1 Mux

## Slide 15: Internal Structure of a 4:1 MUX
A 2n:1 MUX needs 2n, (n+1)-input AND gates for selection and a 2n-input OR gate to generate the final output.  AND/OR logic structure

## Slide 16: Closeness to Decoders
Connect all the input lines of the multiplexer together (to make enable) and remove the OR gate to give you a decoder

## Slide 17: MUX Output Boolean Expression
2:1 MUX
4:1 MUX
General expression for 2n : 1 MUX

## Slide 18: Using 2:1 Muxes to Build a 4:1 Mux

## Slide 19: Practical Application of Multiplexers

## Slide 20: MUX Based Logic Design
MUXes are sometimes called hardware look-up tables.
To implement an n-variable function using a 2n:1 MUX
Use a 2n:1 MUX, connect n input variables to the n select lines
(in the correct MSB-LSB order).
Wire MUX input Di to 1 if function includes minterm mi. All other
inputs are set to 0.
Example: Implement the function using a MUX of appropriate size.

## Slide 21: MUX Based Logic
Advantages:
  Easier to design combinational circuits.
  Easier to debug circuits designed using multiplexers.
Disadvantages:
  Multiplexers can become very large for a large number of inputs.
Good for small circuits.
Normally, any function with more than 4 variable is impractical for direct implementation (i.e., using a single large MUX)
  Use tree of small MUXes or using a variable as MUX data input or Shannon’s Expansion Theorem for implementing large functions.